## Slide 1: Investigating Phosphorus Availability in Biosolids Amended Agricultural Soils
A NEBRA Funded Research Project
Summer 2021
Presented By: Jessica Nekowitsch

## Slide 2: Project Goal
“To research and study phosphorus (P) availability and transport in biosolids amended agricultural soils.”
Specifically:
  Data from 2 farms
  P availability, mobility, testing, and regulations
  Biosolids vs. traditional fertilizers

## Slide 3: Introduction

## Slide 4: Relevant Forms of P
Total P
Insoluble P
Labile P
      Water Extractable P
      Plant Available P

## Slide 5: Methods
Lit Review
Data Analysis
Soil Testing

## Slide 6: Literature Review Findings
N:P ratio
Comparisons
P Concentration Regulations
WWTP Additives
PSI regulations
PSI = PM3/ [FeM3 + AlM3]

## Slide 7: Preliminary Results: P Availability
Chart: NH Farm - South Field Cumulative Excess P2O5 and Soil Test P Over Time
| 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020
Cumulative Excess P2O5 | 168 | 332 | 314 | 389 | 395 | 453 | 599 | 664 | 772 | 923 | 1033 | 1124 | 1287 | 1421 | 1522 | 1623 | 1906 | 2032 | 2237 | 2485
Weak Bray P | 23 | 21 | 27 | 18 | 19 | 32 | 30 | 84 | 65 | 43 | 41 | 20 | 25
Mehlich 3 P | 56 | 55 | 78 | 80 | 56 | 112
Mod. Morgan P | 9 | 17 | 3 | 9

## Slide 8: Preliminary Results: P Availability
Chart: W-5 Excess P2O5 vs. Soil Test P Over Time
| 2015 | 2016 | 2017 | 2018 | 2020 | 2021
Cumulative Excess P2O5 | 119.6437 | 230.8767 | 320.3512 | 320.3512 | 408.2854 | 445.7754
Mod. Morgan P | 24.7 | 29 | 11.5 | 21 | 31

## Slide 9: Preliminary Results: P Mobility
Chart: Soil Test P in VT Farm Fields vs. Setbacks July 2021
| W-5 | W-5 Setback | W-11 | W-11 Setback | W-14 | W-14 Setback
Mehlich III P | 456 | 208 | 391 | 230 | 523 | 300
Total P | 1842 | 1554 | 1705 | 1192 | 1802 | 1345
WEP | 15 | 7.1 | 7.2 | 4.2 | 13.8 | 5.5
PSI | 34 | 16 | 23 | 13 | 28 | 18
Chart: Soil Test P in NH Farm Fields vs. Setbacks, July 2021
| South | South Setback | North | North Setback
Mehlich III | 1600 | 570 | 1570 | 1030
Total P | 5483 | 1447 | 1776 | 1767
PSI | 10 | 3 | 9 | 5
WEP | 1.56 | 0.66 | 2.06 | 1.02

## Slide 10: Preliminary Results: P Test Correlations
PSI = PM3/ [FeM3 + AlM3]
Chart: Total P, Mehlich III P, and Mod. Morgan P vs. WEP for Both Farms (July 2021)
| 15 | 7.1 | 7.2 | 4.2 | 13.8 | 5.5 | 1.56 | 0.66 | 2.06 | 1.02
Mehlich III P | 456 | 208 | 391 | 230 | 523 | 300 | 160 | 57 | 157 | 103
Mod. Morgan P | 705 | 475 | 203 | 123 | 335 | 274 | 340 | 24.5 | 300 | 49
Total P | 1842 | 1554 | 1705 | 1192 | 1802 | 1345 | 5483 | 1447 | 1776 | 1767
Chart: PSI vs. WEP for Both Farms (July 2021)
| 15 | 7.1 | 7.2 | 4.2 | 13.8 | 5.5 | 1.56 | 0.66 | 2.06 | 1.02
PSI | 0.34 | 0.16 | 0.23 | 0.13 | 0.28 | 0.18 | 0.1 | 0.03 | 0.09 | 0.05

## Slide 11: Summary
The Goal
Literature Review
Soil Testing
Data Analysis
Results & Comparison

## Slide 12: Future Recommendations
Further investigate farms with detailed biosolids application and soil testing data
Focus on PSI as an environmental risk indicator for biosolids amended soils
Focus on Mehlich III P tests as plant available P indicators for biosolids amended soils

## Slide 13: Acknowledgements
Andrew Carpenter (Project Mentor, Northern Tilth)
Jim Jutras (Essex Junction WWTF)
Janine Burke-Wells (NEBRA / NEWEA)
Lauren Souther (Northern Tilth)
Mike Potash (RMI)
April Sargent (RMI)
NH Farm
VT Farm
NEBRA and NEWEA
Tracy Chouinard (NEBRA)

## Slide 14: Email Address:
Jessica.Nekowitsch@unh.edu
References